## Slide 1: Initial Sizing

## Slide 2: Aircraft Sizing
One of the most important parts of aircraft design
Determines how big the aircraft is (specifically mass)
Based on the mission requirements
  We know what the aircraft does – its in the specification
  We need to determine how big it is.
One method (the fastest) is to use the mass of the aircraft we will replace
We will use a slightly more sophisticated method
  However, it is still based on using past data
It is also an iterative process

## Slide 3: Take-off Weight Build-up
Break up the take-off gross weight into
Crew
Payload weight
Fuel weight
Empty weight, which includes
  Structure
  engine
  Landing gear
  Fixed equipment
  Avionics
  Etc….. (everything else!)

## Slide 4: Take-off Weight Build-up
Break up the take-off gross weight into
We can express fuel and empty weight as fractions of the gross take-off weight
Which can be rearranged
  Now as the crew and payload weights are usually provided in the specification we need to determine the fuel and empty mass fractions, which in the first instance, we will estimate.

## Slide 5
?

## Slide 6: Empty Weight Estimate
The initial empty weight will be estimated from the fraction of empty to take-off weight fraction.
In future iterations this can be improved by adding the mass of the different components.
Empty weight fraction will be estimated from historical data.
  Typically lies between 0.3 and 0.7 – quite a range!!

## Slide 7: Empty Weight Estimate
Type | A | C
Sailplane – unpowered | 0.83 | -0.05
Sailplane – powered | 0.88 | -0.05
Homebuilt – metal/wood | 1.11 | -0.09
Homebuilt – composite | 1.07 | -0.09
General aircraft – single engine | 2.05 | -0.18
General aircraft – twin engine | 1.40 | -0.10
Agricultural aircraft | 0.72 | -0.03
Twin turboprop | 0.92 | -0.05
Flying boat | 1.05 | -0.05
Jet trainer | 1.47 | -0.10
Jet fighter | 2.11 | -0.13
Military cargo/bomber | 0.88 | -0.07
Jet transport | 0.97 | -0.06
UAV – tactical recce & UCAV | 1.53 | -0.16
UAV – high altitude | 2.48 | -0.18
UAV small | 0.86 | -0.06
Empty weight fraction will be estimated from historical data.
  Typically lies between 0.3 and 0.7 – quite a range!!
  Historical data follows the following trend
  Where A and C are constants which are dependent on the type of aircraft.
Note: variable sweep wings are heavier than fixed wings, to account for this multiply the empty weight fraction by 1.04.
Based on limited data of composite aircraft multiply the empty weight of these aircraft by 0.95.

## Slide 8
?

## Slide 9: Fuel Fraction Estimates
Highly dependent on the mission profile
Therefore need to fly the mission
In the first instance, fuel can be considered to be proportional to the aircraft weight so fuel fraction can be estimated based on the mission flown.
Mission Profiles

## Slide 10: Mission Profiles
Highly dependent on the specification/requirement
Include contingencies, such as,
  30 minutes cruise for VFR flight
  45 minutes cruise for IFR flight
  Loiter, then diversion to alternative airport (commercial IFR)
See regulations (JAR23/25 and FAR23/25 as appropriate)

## Slide 11: Mission Profiles
Mission segments, legs, are usually numbered
Leg 1 usually refers to engine warm-up and take-off
Similarly the final leg corresponds to landing
For initial sizing the following fractions are reasonable for take-off, climb and landing (unless you want to calculate them yourself).
Mission Segment | 
Warm-up and take-off | 0.970
Climb | 0.985
Landing | 0.995
Mission Segment | 
Warm-up and take-off | 0.970
Climb | 0.985
Landing | 0.995

## Slide 12: Mission Profiles
For any mission segment we want to determine the weight fraction which can be determined by the Breguet range and endurance equations.
For range
or
R | = Range
C | = Specific fuel consumption
V | = Velocity
L/D | = Lift to drag ratio

## Slide 13: Mission Profiles
For any mission segment we want to determine the weight fraction which can be determined by the Breguet range and endurance equations.
For Endurance
E or
E | = Endurance
C | = Specific fuel consumption
V | = Velocity
L/D | = Lift to drag ratio

## Slide 14
C?
or

## Slide 15: Specific Fuel Consumption
Specific fuel consumption is the fuel consumption per unit of thrust. This is dependent on Mach number and the type of power plant used as shown below.
Typical Jet SFC (mg/Ns) | Cruise | Loiter
Pure turbojet | 25.5 | 22.7
Low-bypass ratio turbofan | 22.7 | 19.8
High bypass ratio turbofan | 14.1 | 11.3

## Slide 16: Specific Fuel Consumption (propeller)
For a propeller powered aircraft the SFC equivalent to a jet-engined SFC can be calculated from the power specific fuel consumption ().
Where V is the aircraft velocity and is the propeller efficiency (typically 0.8).
Typical Propeller SFC (mg/Ws) | Cruise | Loiter
Piston-prop (fixed pitch) | 0.068 | 0.085
Piston-prop (variable pitch) | 0.068 | 0.085
Turboprop | 0.085 | 0.101
 | Cruise | Loiter
Piston-prop (fixed pitch) | 0.068 | 0.085
Piston-prop (variable pitch) | 0.068 | 0.085
Turboprop | 0.085 | 0.101

## Slide 17: Lift to Drag Ratio Estimation
Many different methods to estimate the cruise and loiter L/D ratio – also see Roskam for alternative method.
How do we estimate the L/D ratio for something we have not designed yet?!?
Aspect ratio? – induced drag….
Wetted area? – parasitic drag…
Neither tells the whole story.
It turns out that the “wetted aspect ratio” is a good predictor of L/D ratio for preliminary design, where,
Where A is the aspect ratio, b is the wing span, and the ratio is the ratio of the wetted area to the reference area.

## Slide 18
?
or

## Slide 19: Lift to Drag Ratio Estimation
Where A is the aspect ratio, b is wing span, and the ratio is the ratio of the wetted area to the reference area.
Each of these lines can be described by
, where
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes

## Slide 20: Lift to Drag Ratio Estimation
Where A is the aspect ratio, b is wing span, and the ratio is the ratio of the wetted area to the reference area.
But where does the ratio come from?
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes
Each of these lines can be described by
, where

## Slide 21: Lift to Drag Ratio Estimation
Where A is the aspect ratio, b is wing span, and the ratio is the ratio of the wetted area to the reference area.
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes
Each of these lines can be described by
, where

## Slide 22: Lift to Drag Ratio Estimation
Where A is the aspect ratio, b is wing span, and the ratio is the ratio of the wetted area to the reference area.
The most efficient cruise and loiter velocities for jet and propeller aircraft occur at different conditions.
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes
 | Type
15.5 | Civil jets
14 | Military jets
11 | Retractable prop aircraft
9 | Non-retractable prop aircraft
13 | High aspect ratio aircraft
15 | Sailplanes
Each of these lines can be described by
, where
 | Cruise | Loiter
Jet |  | 
Prop |  | 
 | Cruise | Loiter
Jet |  | 
Prop |  | 

## Slide 23: Fuel Fraction Estimate
By multiplying the flight segment weight fractions together the fuel weight fraction can be obtained, including a 1-2% factor to account for unusable/trapped fuel etc.

## Slide 24: Putting it all together
We have two equations relating empty weight to the gross take-off weight
(from regression of historical data)
(from the weight build-up calculations)
We need a solution which satisfies both equations we can do this by
Producing a table of guesses, from these calculating the empty weight fraction (using the first equation above), then using the second to calculate - and find where the gross take-off weight is the same.
Plot the weight empty weight fraction from both equations and see where they cross.